## Slide 1
Crystallization Facility
and use of Liquid Nitrogen
Tom Walter
(with many thanks to Karl Harlos)
1st-February-2023

## Slide 2
Sitting-drop vapour-diffusion method
The protein concentrates up in the presence of different components (pH, salts, polymers, etc) to encourage crystal nucleation and growth
Hydra transfers reservoir solutions
From Deepwell Plates
To the 96-well crystallization plates (up to 3 at a time)
Adaptors for different crystallization plate types
Over 1200 different conditions to try
Cartesian dispenses nano-litre drops
Non-contact dispensing
typically 100 nL + 100 nL for screening, 15 uL protein per plate
Also does basic optimization experiments
  Additive and detergent screens
  Grids based on “hit” condition
  Grids varying multiple components
Setting up Crystallization Plates

## Slide 3
Crystallization is now (temporarily) on an isolated IT network
To use the facility you need to register as a user (on the isolated network)
Strubi – xtalPIMS – Login – Register
Before experiment you need to register sample and aliquot :
Strubi – Internal – Sample Registration- login – click on the name of your project – Add New Sample or click on existing Sample – Add new aliquots
NOTE “Sample” = construct(s), “Aliquot” = prep
For access and instructions contact Tom Walter ‘walter@strubi.ox.ac.uk’ or Karl Harlos ‘karl@strubi.ox.ac.uk’
ONGOING in 2023! A major rewrite and upgrade of the crystallization IT to (re)enable remote monitoring of the crystallization experiments. You should see more changes this year!
Access (post-IT disruption)

## Slide 4
Monitoring your experiments
Contact Tom Walter or Karl Harlos to retrieve plates
@20 ºC
3 x RI1000 systems (Formulatrix)
in the former X-ray room
total capacity is 3000 plates,
Plates can be imaged for at least 12 months and are then stored on open shelves for another 4-6 months.
Please do not try and operate the system yourself, unless authorized by Tom Walter or Karl Harlos.
Cold room (6.5 ºC)
1 x Formulatrix RI1000-0014
Lab2 large cold room
capacity 1000 plates
Plates can be imaged in the system for at least 1 year and are then stored in the cold room for another year.
Plates are transferred in a cool-box and left to equilibrate. Please label box with name and date.
Please do not leave cold room door open to keep humidity low.

## Slide 5
Images of your drops can be viewed in ‘xtalPIMS’ currently only available on the isolated IT network – AVAILABLE OVER VPN/REMOTE DESKTOP VERY SOON (waiting on MSD-IT…)
Look up conditions, mark drops, view timecourses, etc

## Slide 6
(3) X-ray-plates for in situ
diffraction
low background scattering
need special sealing tape
Other plates and crystallisation methods
(1) Swissci-plates – 3 drops, preferred by Diamond for eg Xchem fragment screening
(2) Hydrophobic and round bottom Greiner plates – for detergents
(4) Lipidic Cubic Phase (LCP) Crystallisation for Membrane Proteins
Basic set of tools and consumables are available from Karl’s office and Christian Siebold’s group
“Gryphon” instrument for automated LCP
Syringes to mix mono-olein
with sample
Glass plates and tapes
Notes: 6

## Slide 7
New Instruments
Scorpion for optimisations and making deep-well blocks (In progress)
Crystal Gryphon for LCP crystallisations – (for advice be nice to the Siebold group!)

## Slide 8: Looking-at, Manipulating and Freezing Crystals
Please use sharps bins
Olympus stereo-microscope
Mitegen dual thickness loops
(See Karl)
Razor blades
and needles
Cold room Nikon stereo-microscope
SPINE-standard UNIpucks, pins and caps

## Slide 9
Pins and Pucks
Write details of crystals on
puck-sheet and copy information to ISPyB. (The hard-copy is often useful during screening and to make notes!)
SPINE standard pins
Uni-pucks,
when freezing crystals try to avoid build up of ice.
Please check that puck is not damaged,
i.e. that all magnets and clips are in place
Puck canisters
Please, where possible, recycle pins and re-use loops, and re-use your grid boxes

## Slide 10
Future = pucks for EM-grids
12 grid boxes per puck
10 pucks per cannister (but best to avoid the top position)
Karl is overseeing the transition to this system – please cooperate!

## Slide 11
Liquid Nitrogen Safety-1
Follow local rules:
read safety sheets displayed outside former X-ray room, wear cryogloves and safety glasses,
Liquid nitrogen can be taken from
small dewars in the former X-ray room
small dewars in the OPIC prep lab or
(b) from the tipper in room 1.04A.
You need to attend the ‘Cryo-safety workshop’
organised by WCHG Safety Officer
before you are given card access to 1.04A.
Take extra care when taking a foam dewar with LN2 through the lab
Tipper in room 1.04A
NEXT COURSE 27th FEBRUARY (probably...)

## Slide 12
LN2 takeoff point in room 1.04A
SALTO lock operates with swipe card, please contact Karl or Tom if you want to be trained and already have access to 1.04A.
‘Dry’ Liquid Nitrogen for EM-grids
F30 EM prep room

## Slide 13
Freezing Crystals in Cold Room
(a) put up warning notice on cold room door
(b) use Oxygen sensor on bench near working area at all times
Liquid Nitrogen Safety-2
Portable Oxygen sensor
Similar procedures will be put in place in crystallization room if there are AHU works

## Slide 14
Liquid Nitrogen Safety-3
Glacios-EM Room 00/097
LN2 supply-dewar for Glacios-EM
Present safety measures include:
(1) Several handheld Oxygen monitors
(2) an Oxygen monitoring
system within the room,
which will trigger an alarm
in case of low Oxygen
(3) Automatic shutoff valves
at the LN2 dewar
(4) Warning signs on all
doors to Lab-2 and
on all doors to the
Glacios room

## Slide 15
Storing and Transporting frozen Crystals and EM-grids
Safety note:
Dry shippers must only be transported in the ‘dry’ state,
i.e. any ‘liquid’ must be poured away before transport.
They will maintain temperature for several days.
Dry shippers, 4L-dewars & transfer dewar in former F30 room (OPIC).
Discard small amounts of excess Liquid Nitrogen into dewar with funnel. Larger amounts can be disposed of in the LN2 room 1.04A.
Storage dewars for crystals and EM-grids (F30 room OPIC)

## Slide 16
Yellow suite LN2
Small cramped area in service corridor with LN2 storage and pressurised dewar
Get training & advice
Always use the extraction system when dispensing LN2 from pressurised dewar
Tell someone else that you are working there especially out of hours! (Preferably don’t do it out of hours!)
Storage dewars will be upgraded to puck system in due course

## Slide 17
Thermofluor – thermal shift analysis for proteins and viruses (Agilent MX3005P RT-PCR machine)
UNCLE light scattering and native (i.e. no dye) thermal shift
DLS – particle sizing and polydispersity
Nanodrop spectrophotometer
Label printers
Brother P-touch 200 available in Karl’s office
Barcode label printer available in Crystallization area
Other Instruments

## Slide 18
Mechanical Workshop
in Green Building
Two groups:
Department of Oncology – CAD-CAM facilities - John Prentice
Institute of Biomedical Engineering (IBME) - James Fisk